## Slide 1
Navitrol navigation system

## Slide 2: Positioning
Positioning uses natural features and map matching algorithms to determine the x,y and heading
Reflectors can be used to improve positioning if the environment does not provide enough natural features
Position accuracy is ±1cm, heading accuracy 1 degree and maximum speed can be 3m/s.
Position can be updated up to 30 Hz rate

## Slide 3: Other features
Navitrol reports position confidence
Navitrol reports any operational errors
Environment can be divided into floors
Remote monitor tool for showing diagnostic data in real time

## Slide 4: Dead reckoning
Navitrol expects to get dead reckoning measurements from AGV
There are some options how to achieve this
  AGV sends dead reckoning pose to Navitrol over Ethernet and Navitrol replies with corrected pose (implemented)
  Navitrol reads the distance traveled and the steering angle from Ethernet and calculates the pose itself
  Navitrol reads the raw data from sensors

## Slide 5: Position initialization
Position must be initialized
Initial position must be given with 1m position accuracy and 10 degrees of heading accuracy
After the initial position is given Navitrol finds the accurate position

## Slide 6: Environment teaching
Navitrol is set into teaching mode
Navitrol records the dead reckoning position and scanner measurements
The AGV is driven manually through the operation area
Teaching is stopped
Data is saved to a laser data file.

## Slide 7: Map editing (start)
Navithor map tool shows the raw laser and dead reckoning data
Also CAD data can be shown on the map.

## Slide 8
Map editing (selecting measurements)
User can select any number of measurements for editing

## Slide 9
Map editing (auto match)
Auto match tool matches the measurements
to each other correcting dead reckoning errors

## Slide 10
Map editing (manual editing)
Manual editing allows to do the last fine tuning

## Slide 11
Map editing (generating map)
Map is generated from the corrected measurements

## Slide 12
Map editing (reflectors)
Reflectors (green) are selected from the map

## Slide 13: Exporting map
When the map is ready it is saved into a file
All the editing steps in the example were done in less than 2 minutes
The map file is moved to Navitrol
Navitrol is restarted and the new map is used for positioning

## Slide 14: Remote monitor
Remote monitor shows the live laser data and measurements from Navitrol