## Slide 1: Sequence diagram - Coupling
Navitrol
AGV
AGV
Navitrol
Production system
Production system
Navitrol controls and docs the AGV to the pick up point
1. Production order to pick up point
4. Trailer coupling action – Prepare for coupling
5.Trailer coupling status – Ready for coupling
AGV performs coupling preparations
Navitrol starts reversing towards the trailer aiming for the kingpin
6.Trailer coupling status – Kingpin detected
AGV tries to detect the kingpin
Navitrol stops the AGV
7. Trailer coupling action – Couple
AGV locks itself to the trailer
8.Trailer coupling status – Coupled
9.Trailer dimensions
2. Start pick up command
10.Pick up ready
Navitrol is now able to transport the trailer
3. Trailer dimensions request

## Slide 2: Sequence diagram - Blank
Navitrol
AGV
AGV
Navitrol
Production system
Production system
2.
3.
1.
4.
5.
6.
Blank